## Slide 1: Opposition report
About group: B by: Ylva Reinhold

## Slide 2: Steam Iron

## Slide 3: Evaluation
Key strengths
Structured Approach
  The report has clearly defined sections that align with the project expectations (e.g., BOM, DFA, sequencing, layout).
  Methodologies are appropriate and well-documented, with equations, assumptions, and calculations clearly explained.
Exploded CAD model with balloons and parts list is well-made.
Parts Coding
  is well thought-through, structuring the part numbers according to the subassembly they belong to.
Use of Multiple Line Balancing Methods
  LCR, Kilbridge, RPW, and custom method (to overcome impracticalities of standard methods due to short tasks and mixed subassembly assignments) with comparison.
Solid DFA Analysis
  The Boothroyd-Dewhurst and Eskilander methods were applied correctly, and results were cross-validated with measured assembly times.
Sensitivity and Break-even Analysis
  It is very detailed, accounting for different production levels.
Extra work beyond requested points
  PFMEA: The failure mode analysis is well-developed. While it is nice to have this, it would serve a better purpose, if the knowledge gained through it was more clearly linked to the redesign proposals and to potential mitigation strategies in the process design (or at least referred to in a discussion part).
  VSM: Nice that they have done it, although it is not really necessary.
Nice visuals (especially for the layout solutions)

## Slide 4: Evaluation
Areas for improvement
Technical issues or missing information:
  It might be nice to have some more detailed CAD views of the subassemblies for increased understanding of the product structure.
  LSD only considers one sub-assembly, it might be nice to have a subset of a few (of course not all) sequencing options of the whole product.
  The solution for the ‘Semi-Automated Layout with Robotic Logistics’ is not true to its name, as it does not include any automated assembly but only automated part handling. Thus, the cost calculations for automatic feeding and insertion do not make sense (the only thing the robots do is moving already prepared kits between buffers and conveyors). You should recheck that.
  In the DFA evaluation for automated assembly, provide a more detailed analysis/ result of which parts or subassemblies show suitability for assembly (or not).
  Add a discussion section where you reflect on and connect the results from different sections of the report, apart from just the cost comparison.
Practical feasibility concerns
  Performing the make or buy decision on the part level doesn’t make so much sense since you don’t produce the actual parts but only the subassemblies and the final assembly. If it was applied to the subassemblies, that would make more sense.
  In the manual layout solution, you are wasting a lot of space which will increase transportation time and inflate the overall throughput time.
Gaps in explanation
  Limited validation of cost data sources: The economic analysis is good but could benefit from more benchmarking or references.
  The redesign proposals could be strengthened. Although you identified critical operations for redesign, they fall a bit short in explaining the specific design suggestions for component changes or alternate assembly techniques (eg. CAD model).
  The technical justifications for why you chose certain strategies for the final flow and, eg. material handling could be a bit more detailed. Maybe by comparing them to other options.

## Slide 5: Evaluation
Areas for improvement
Clarity and flow
  Some tables and diagrams (as referenced in the text) are in appendices. For improved readability and quick comprehension, it might be better to integrate the key visuals into the sections.
  Introduce the precedence diagram at an earlier stage so the reader can understand the constraints before you go into line balancing.
  In the DFA evaluation for manual assembly, you could enhance clarity by showing how you actually calculated the assembly efficiency and the min Number of parts.
Formatting
  Check your referencing of figures, appendices, etc.
Assessment of implementation and results
Process Documentation
  The report demonstrates complete documentation, from product analysis and process flow and layout to cost analysis.
Valid and logical results
  Data sources (e.g., Statista, standard DFA tables) are acceptable, although further sources in the market analysis would be ideal.
  The overall logical structure and reasoning are coherent, however a few logical mistakes can be improved upon.
Alternative solutions
  The report does successfully compare multiple line balancing methods and layouts, but alternative product designs or manufacturing processes (e.g., snap-fits vs. screws) are a bit underexplored in redesign or DFA improvements.

## Slide 6: Evaluation
Report and presentation
Structure and Readability
  The report is organized and readable, with clear headings.
  The overall flow of ideas is logical, covering problem definition, analysis, and solution, but the reflection could be improved.
  The report could benefit from being restructured to some extent. The redesign chapter, for example, should be introduced before the discussion/ final conclusion as it might provide some additional input. Rethink the flow of the report and how the different chapters play together.
Figures, Tables, and Diagrams
  Figures and diagrams effectively support arguments, though better placement of some key visuals in the body could enhance clarity.

## Slide 7: Questions for discussion and suggestions
How did you measure the (actual) processing times of each operation?
Have you considered automating some of the actual assembly tasks?
Are you planning to work more on the redesign?
Recommendations
Add some more detailed CAD views of the subassemblies
Recheck your logic on the ‘semi-automated’ solution (you only automated part handling but no assembly tasks)
Spend more time on the actual redesign (potentially in CAD) and connect it more closely to the outcomes of the PFMEA and DFA analyses
Include an overall discussion and reflection of results in the end to logically connect the distinct results from different report sections
Final verdict
This is a solid report, showing thorough understanding of assembly technology principles. While some improvements could be made in market justification, a few minor logical errors, and visual integration, the project as a whole reflects a good implementation of project deliverables.
Questions